## Slide 1: Photonic reformatting: Astrophotonic spectroscopy and Adaptive Optics
Jeremy Allington-Smith (Durham University)
with contributions by: Graham Murray, Rob Harris, Dave McLaughlan, Robert Thomson, Tim Birks, Itan Gris Sanchez, Tim Morris, Alistair Basden, Eric Gendron
Illustration based on Time’s Eye by Salvador Dali © Salvador Dali, Fundacion Gala-Salvador Dali, VEGAP, Barcelona 2010
In regione caecorum rex est luscus (Desiderius Erasmus)

## Slide 2: Why Florence?
Galileo Galilei buried here (S. Croce)
Medici family’s motto:
Home of the Risorgimento
Will Astrophotonics tread the same path?
κοσμος κοσμου κοσμος

## Slide 3: Contents of this talk
Why Integrated Photonic Spectroscopy is good….
… but not always: There are no free lunches
Focus on high resolution
Photonic reformatting with Adaptive Optics
(See talks by Roger Haynes, Robert Thomson, Itan Gris Sanchez)
Are…. but first, a word about FRD

## Slide 4: FRD and thermodynamics
Etendue not conserved -> information is lost
OR requires more money

## Slide 5: Integrated Photonic spectroscopy
IN PRINCIPLE
Significant advantages especially for ELT cosmology
  Miniaturisation -> mini-spectrograph ideal for ELT cosmology
  No optics, highly integrated device with simple geometry
  Mass production by laser inscription for multiplexed applications
Also: elimination of modal noise?
Application to high-precision spectroscopy?

## Slide 6: Integrated Photonic Spectrograph
Based on Arrayed Waveguide Gratings (AWG) used extensively in telecommunications
Analagous to traditional bulk disperser
Highly integrated, no optics
Replace output waveguides with 1-D detector
Replace input waveguides with reformatted slits
Requires single-mode input
Freespace Propagation Zone
Waveguide
array
Input
waveguides
Output
waveguides
See papers by Bland-Hawthorn, Czetojevic, Lawrence et al.
See Roger Haynes’s talk

## Slide 7: Conversion to single modes
One thick waveguide
supporting N modes
N thin waveguides, each supporting 1 mode
Transition zone
Core with high refractive index
Substrate with low refractive index
MMW
SMW
IMW
See Leon-Saval, Bland-Hawthorn, Czetovic, Lawrence, Haynes et al.
Multimode
Many single modes

## Slide 8: Electric field MMW
Using slab model:
Colours indicate
Different modes

## Slide 9: Electric field IMW
Same scale

## Slide 10: Electric field SMW
Same scale

## Slide 11: Modal evolution
Single degenerate mode in each output
Many non-degenerate modes
Core
Substrate
Effective refractive index
Outer diameter
MMW
SMW

## Slide 12: Wave model
Maxwell’s equations
Wave equation
Helmholtz equation
Helmholtz equation for core and cladding
Geometry+ boundaries
Unified dispersion relation
Weak guiding
Field distribution in cladding
Field distribution in core
e.g. Snyder, A. W. and Love, J. D., [Optical Waveguide Theory], Chapman and Hall Ltd. (1983).

## Slide 13: More realistic case (2D)
2-D geometry using multicore fibre (Leon-Saval et al. OpEx 18, 8430 (2010))
Degenerate supermode
MM
SM

## Slide 14: Other ways
See e.g.
Noordegraaf et al. OpEx 17, 1988 (2009); OpEx 18, 4673 (2010)
Leon-Saval et al. Opt Lett 30, 2545 (2005)
Jovanovic OpEx 20, 15 (2012)
Birks et al. OpEx 20, 13996-4008 (2012).
Thomson, Kar, and Allington-Smith, OpEx 17, 1963-1969 (2009).
Courtesy of Birks et al.

## Slide 15: Fractional energy vs mode count
Calculated using overlap integral between waveguide and propagating mode
Example calculation for 50μm FWHM
Moffat has very extended wings as Gaussian but same FWHM

## Slide 16: No free lunch
So we need 12 copies of the reciept?
But I didn’t have a starter
Who ordered the 5000 anchovies?
There is no such thing as a free lunch. Anon. in response to Henry Wallace, US vice-president, 1943)

## Slide 17: No free lunch 1
To first order IPS is as large as traditional instrument
Focus on applications where mode count small – near to diffraction limit
Celestial light is Multimoded (aperture >> diffraction-limit)
Each mode to be dispersed separately
Alternately, can use multiple-input AWG and cross-disperse but bulky
ispersedField
Field
Field
Photonic lantern
AWGs
1D detectors
Longslit
Diverse
field
Multiple
object
Input focus
Reformatter
/switcher
Slit Spectrograph
2D Detector
Field
Single
object
Multiple
object
Traditional
Astrophotonic

## Slide 18: Image slicing: optimised spectroscopy
1 spectrograph with N slices
N spectrographs with 1 slice each
Slicing
(N)
Example has N=3
Maximise throughput x spectral resolution or integral field spectroscopy

## Slide 19: Image slicing/dicing technology

## Slide 20: Image slicing: reduce disperser size
Twice the slit length
Half the slit width
Half the disperser size
y(λ)
z
x
z
Or double number of spectrographs
This example for double-pass Littrow echelle grating with N=2
Disperser
fS
DS
Collimator
Important for ELTs

## Slide 21: Reformatting slit (dicing)
Segment field, reformat into slit
If image resolved -> spatially-resolved-spectroscopy with optimal throughput and tradeoff between spatial resolution and spectral resolution
If image unresolved (e.g. poor seeing) -> optimises spectral resolution x throughput
  Advantage:
    increased throughput
    Improved spectral and/or spatial resolution
  Disadvantage:
    Needs extra detector pixels -> more noise, cost
    Complex optics, reduced throughput

## Slide 22: No free lunch 2
Number of diffaction-limited subsets
(size dD) Into which field is split
Area of fibre core
Area of each diffraction-limited subset
Number of modes required = number of diffraction-limited pieces
Number of modes
In cylindrical waveguide
of diameter dF
Θ =Limiting numerical aperture
FT = focal ratio of collimator

## Slide 23
MNRAS 428, 3139 (2013)

## Slide 24: Calculation of IPS sizes
For normal applications, is as big as traditional instruments
Number of detector pixels very large
Relative scale lengths
Number of detector pixels
Semi-photonic instruments
Reference instrument

## Slide 25: Reducing the number of modes

## Slide 26: Reduced-mode applications
Use with Adaptive Optics - natural option
Currently prototyping photonic reformatter to form idealised narrow slit for high precision spectroscopy -> See Robert Thomson’s talk
Complementary to other work on photonic spectroscopy (Sydney, Potsdam..)
Additional incentive: Use photonic reformatter as a Wavefront Sensor?

## Slide 27: Adaptive Optics: Canary
Adaptive Optics testbed for ELT on WHT (Durham/Paris)
SCAO
LTAO (4L3T)
GLAO (4L3T)
Strehl: 27%
Strehl: 17%
Strehl: 21%
Turbulence Profile @ 06h30m UT 07/10/2014
Recent results (Oct 2014)
Laser altitude 14km
Several flavours of LTAO investigated
  3 tip-tilt only NGS and 4 high-order LGS
  3 high-order NGS and 4 high-order LGS
  3 high-order NGS only
All compared to SCAO using ‘truth’ WFS
LTAO: First ever on-sky demonstration
Thanks to Tim Morris, Eric Gendron…
LTAO = Laser Tomograohy
GLAO = Ground-layer
SCAO = Single-Conjugate
50”
45”
39”
MV= 11.43
MV= 8.86
MV= 10.62
24”
α=06 48 17.3, δ=+41 04 59

## Slide 28: Photonic reformatter tests with Canary
See Robert Thomson’s talk
PHOTONIC LANTERN: Good coupling efficiency observations into a single-moded slit
  Very preliminary analysis…
Corrected
Uncorrected
15%
34%
Output single-mode slit
Waveguide network made
By Ultrafast Laser Inscription
(Herriot Watt)
Photonic Lantern
(Bath)
Canary AO
(Durham/{Paris)
Reference 1550nm PSF
Uncorrected
Corrected
Intermediate single modes
Uncorrected
Corrected

## Slide 29: Waveguide reformatter as AO WFS?
Reformatter measures power in modes which are low-order in the SMFs but low or high order in the MMF
How to determine link between aberration and SM output? (“Poke matrix”; “Timplex”…)
Sensitive to details of geometry, flexure and temperature ?
Low-order in single-mode fibre
(Degenerate)
Simplify wavefront sensing using output from slit itself?

## Slide 30: Defeat modal noise?
1 snapshot
Modes partly coherent -> interfere to form speckle patterns
These changes unpredictably to cause statistical error due to number of speckles within field or pupil stop
  Adds noise to spectrophotometry
  PSF uncertain: sky subtraction error
Solution: mechanically agitate to smooth out speckle pattern on all time scales - but difficult for highly muliplexed spectroscopy
  ρ
M = number
of modes
10 snapshots
100 snapshots
History: Baudrand and Walker (1972); Goodman and Rawson; Grupp,
Lemke, Corbett, Allington-Smith and Murray 2011 MNRAS 417, 689,
See also Ramsay et al.

## Slide 31: Modal noise: visibility model
Decoherence due to
different propagation constants of modes (analoguous to ray angles)
Spectral content (visibility increases with R
Visibility due to decoherence:
Prediction for M = 900 (measured from speckles)
Lemke et al. 2011 MNRAS 417, 689
LNA
theoretical SNR, vC
Obtainable SNR = --------------------------------
measured visibility
But modes do not coherently interfere in photonic dicer..?

## Slide 32: Conclusions
Adaptive Optics and Photonic spectroscopy are a natural combination for precision spectroscopy
A lot of work still to be done
The end